## Slide 1: LAZARUS Practical Side-channel Resilient Kernel-Space Randomization
David Gens
Christopher Liebchen
Ahmad-Reza Sadeghi
Orlando Arias
University of Central Florida
Intel Collaborative Research Institute for Secure Computing
Technische Universität Darmstadt
Dean Sullivan
Yier Jin
University of Florida
Notes: This work was done alongside our collaborators in David Gens, Christopher Liebchen, and Dr. Sadeghi at TU Darmstadt; as well as Dean Sullivan and Dr. Jin at UF.

## Slide 2: Run-time Attacks Against the Kernel
Vanilla Kernel
User Mode
Code
System Call
RX
...
RX
Data
Code Pointers
RW
…
RW
Code will execute with malicious input (e.g., a ROP-payload)
Trigger system call to use to the malicious code pointer
Exploit kernel vulnerability to manipulate code pointers
Code Pointers

## Slide 3: Run-time Attacks Against the Kernel
Randomized Kernel
User Mode
Code
System Call
RX
...
RX
Data
Code Pointers
RW
…
RW
Code Pointers
?
?
?
?
?
?
?
?

## Slide 4: Run-time Attacks Against the Kernel
Randomized Kernel
User Mode
Code
System Call
RX
...
RX
Data
Code Pointers
RW
…
RW
Code Pointers
?
?
?
?
?
?
?
?
Kernel Execution leaks information through hardware side-channels

## Slide 5
2013
2014
2016
Practical timing side channel attacks against KASLR
Hund et al. (IEEE S&P)
TSX improves timing attacks against KASLR Rafal Wojtczuk (Bromium Labs)
Prefetch
Gruss et al. (ACM CCS)
TSX Attack
Jang et al. (ACM CCS)
BTB Attack
Evtyushkin et al. (MICRO)
KASLR Attacks Timeline
SELECTED

## Slide 6: TSX Attack (Jang et al.)
Intel’s Transactional Synchronization Extension (TSX) hardware lock elision for threaded applications
Transactions inside TSX blocks are guaranteed to complete atomically
If they can not be completed atomically, the transaction is rolled back and an abort routine is run
  L1 cache miss
  System call
  Illegal memory access
    This exception is masked from the operating system

## Slide 7: TSX Attack (Jang et al.)
From userland, start TSX block
Dereference possible kernel address
  This will fail
  Exception masked by TSX block
Transaction aborts
  Get timing measurement
There is a measurable timing difference when looking at kernel pages

## Slide 8: Prefetch Attack (Gruss et al.)
Intel CPUs have the prefetch instruction
Intel CPUs also have a clflush instruction
Both instructions can be run from ring 3 targeting any address
Cache contents will affect the timing of the prefetch instruction
Notes: And yes, prefetch can target addresses that are mapped in kernel space.

## Slide 9: Prefetch Attack (Gruss et al.)
Flush cache
Execute target code
Prefetch probed address
Measure timing
  If address was previously cached, timing will be shorter

## Slide 10: Related Work: First Defenses
Prohibit Timing
Functionality
Privilege-level separation in the caches
Address-space
Separation
Fix PFH
!
Ineffective [Wojtczuk, Jang et al]
!
Breaks Existing Software
!
High Run-Time Penalty [Gruss et al]
!
Modifies Hardware (costly & legacy problem)
Operating System
Software

## Slide 11: Our Approach: LAZARUS Making KASLR resilient to paging-based side channels

## Slide 12: LAZARUS: Contributions and Challenges
Practical side-channel resilience for KASLR
Avoids Performance-heavy Context Switches
Prototype Implementation
  LAZARUS for the Linux kernel
  Tested using Real-World Setup
  Extensive Performance and Security Evaluation
Notes: „Performance-heavy context switch“ -> we do not require a separate PT-hierarchy and do not reload CR3 with a new value, hence, the address space actually stays the same

## Slide 13: Paging in AMD64
PGD Offset
Frame Offset
PGD0
PGD1
PGD2
…
cr3
Physical Frame
Virtual Address
PUD Offset
PTE Offset
PMD Offset
PUD0
PUD1
PUD2
…
PMD0
PMD1
PMD2
…
PTE0
PTE1
PTE2
…
47
0
Notes: The virtual address is divided into portions. The upper 10 bits offset into the Page Gobal Directory. The PGD entry will point to a set of page table entries. The second upper 10 bits become the offset into the PTE. AMD64 uses 48 bits for page addressing and a 4 level hierarchy instead of 2 to resolve the physical frame. Whenever a new task is scheduled into the CPU, cr3 is reloaded with the base address of the Page Global Directory for the process that is about to run. Reloading cr3 has the side effect of flushing all non-global TLB entries. Kernel pages are marked as global.

## Slide 14: LAZARUS: Design
Processor
Kernel Thread
User Process
LAZARUS
Physical RAM
Core
MMU
Process PGD
Kernel PUD
Kernel PMD
Kernel PTE
User PUD
User PMD
User PTE
User Memory
Randomized Kernel Memory
In effect, we have two different set of page tables for a process.
x86[-64] only has one cr3 register!

## Slide 15: LAZARUS: Implementation
Prototype for the Linux kernel
  Version 4.8
    Completely transparent to applications
  Modifies low-level entry paths
    Unmap kernel page tables during Ring-3 execution
  Hide switching code using dummy entries
Notes:   In our implementation of CATT we built a prototype for testing our approach in the Linux kernel.
  We started our work last year, and were using the most recent kernel version at that time, which was 4.6
  Our changes are completely transparent to applications and require no changes to any other software or hardware components
  We modified the physical page allocator in the kernel to associate individual page frames with a security domain tag
  And we added a dedicated kernel zone the the buddy allocator to partition the DRAM

## Slide 16: LAZARUS: Implementation
User PUD
…
Process
PGD0
PGD1
PGD2
…
cr3
PGD511
Kernel
Userland
Not mapped
Kernel
Entry Stub
Kernel PUD0
Notes: Normally, a process virtual address space looks as pictured. <ADVANCE> What we do with Lazarus is change the address map a bit. Instead of mapping the kernel at the top of memory, we map a stub to go map the kernel for us. Whenever any kind of event that needs the supervisor to perform an action, the entry stub executes. The entry stub modifies the last PGD entry to point to the kernel‘s PUD. At this point kernel code and data is mapped to memory and can be safely executed. The stub proceeds to call the necessary execution path in the kernel. When the kernel exits, the stub takes over and replaces the last PGD entry with a user one. This unmaps the kernel once again, leaving the stub. We can now safely return to userland. It‘s imperative to note that this action does not require changing the value stored in cr3 for most cases. The only time that cr3 is changed is when a scheduling event occurs. CHECK: This has the benefit that we do not have to flush the non-global pages out of the TLB whenever LAZARUS maps or unmaps the kernel.

## Slide 17: Evaluation
Notes: In our evaluation

## Slide 18: Security
Run attacks against LAZARUS
Chart: Address (Offset)
Kernel Entry Point

## Slide 19: Performance
Chart: 
| perlbench | bzip2 | gcc | mcf | gobmk | hmmer | sjeng | libquantum | h264ref | onmetpp | astar | xalancbmk | bwaves | milc | zeusmp | gromacs | cactusADM | leslie3d | namd | dealII | soplex | povray | calculix | GemsFDTD | tonto | lbm | sphinx3
 | 0.98361 | 0.99524 | 0.99725 | 1.0026 | 1 | 1 | 1 | 0.99643 | 1.0022 | 1 | 1 | 1 | 0.99737 | 1 | 1 | 1 | 1 | 0.99763 | 1 | 0.99751 | 0.99726 | 1.0051 | 0.99882 | 1.0094 | 1 | 1 | 1
BMKNAME | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928 | 0.99928
SPEC2006 CPU Benchmark
~-0.1% Overhead
Notes: These are some very good results, but -0.1% overhead? Even if we treat perlbench as an outlier, something may be wrong. And there is: there is a caveat we must discuss. The SPEC2006 benchmark is designed to test the performance of your CPU, and memory system, not your operating system as a whole. The results we are seeing here can very well be within experimental error. For this reason, we decided that further testing was necessary. This time, using a benchmark that will stress test the operating system.

## Slide 20: Performance
Chart: 
| syscall | read | write | stat | fstat | open/close | select10fd | select100fd | select250fd | select500fd | select10tcp | select100tcp | select250tcp | select500tcp | handler_inst | handler_ov | prot_fault | fork+exit | fork+execve | fork+/bin/sh
 | 2.6662 | 2.1872 | 2.6063 | 1.4612 | 2.2288 | 1.4318 | 1.5813 | 1.178 | 1.079 | 1.0649 | 1.5304 | 1.1038 | 1.0336 | 1.0155 | 2.0272 | 1.2009 | 1.1094 | 0.84467 | 1.0612 | 1.0383
 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725 | 1.4725
LMBench3 Suite
~47% Overhead
Notes: The LMBench3 does stress test the operating system. We now get about 47% in performance overhead. This looks high, but we must remember what is happening behind the scenes. This particular benchmark is constantly requesting Kernel Services in a tight loop. Applications do not work this way. Although the benchmark gives us an idea of the effects of our changes at an extreme case, it is not indicative of regular actual workloads.

## Slide 21: Performance
Chart: 
| aoi-stress | sqlite | fs-mark | dbench-12 | dbench-48 | dbench-128 | dbench-1 | iozone-read | iozone-write | iozone-dt-read | iozone-dt-write | unpack-linux | postmark | stream-copy | stream-scale | stream-triad | stream-add | npb | hmmer | mafft | gmpbench | john-the-ripper | gm-hwb-cs | gm-o-hwb-cs | gm-lat | himeno | c-ray | cmprss-pbzip2 | cmprss-gzip | cmprss-lzma | crafty | dcraw | encode-mp3 | encode-ogg | ffmpeg | minion | sudokut | openssl | phpbench
 | 0.99167 | 0.98086 | 1.0045 | 1.0654 | 1.0683 | 1.0991 | 1.0168 | 1.2781 | 1.0061 | 1.2775 | 1.0042 | 0.98761 | 1.1475 | 0.99903 | 0.99809 | 1.0006 | 0.99898 | 0.77845 | 1.0111 | 1.0064 | 0.99937 | 1 | 1 | 1 | 1 | 1.0271 | 1.0001 | 1.012 | 1.0081 | 1.0095 | 1.0017 | 1.0067 | 1.0043 | 1.0033 | 1.0101 | 0.99969 | 1.0112 | 1.0057 | 1.0024
Column1 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211 | 1.0211
Phoronix Suite
~2% Overhead
Notes: The Phoronix Test suite is a bit more inclusive. For our purposes, we only ran the system and disk benchmarks. This gives us a better idea of how the system behaves. The Phoronix suite has a decent balance between CPU intensive tasks and OS intensive tasks. Again, we find benchmarks that are heavy on the latter behave worse, specifically those that perform reads.

## Slide 22: Performance
Run pgbench in a PostgreSQL database: 2.386% overhead
2x better than Gruss et al. while offering the same security guarantees!
Notes: The Phoronix Test suite is a bit more inclusive. For our purposes, we only ran the system and disk benchmarks. This gives us a better idea of how the system behaves. The Phoronix suite has a decent balance between CPU intensive tasks and OS intensive tasks. Again, we find benchmarks that are heavy on the latter behave worse, specifically those that perform reads.

## Slide 23: Conclusion
Beware your benchmarks for they may lie to you!
Attacks against KASLR are possible using architectural side channels
Still possible to defend against them without having to change hardware
LAZARUS does such thing, while offering negligible performance overhead

## Slide 24: Questions?