## Slide 1: ATRIUM: Runtime ATtestation ResIlient Under Memory Attacks
Shaza Zeitouni, Ghada Dessouky, Orlando Arias, Dean Sullivan, Ahmad Ibrahim, Yier Jin, Ahmad-Reza Sadeghi

## Slide 2: Remote Attestation
Prover (untrusted)
Measure software state:
hash(code binary)
Challenge
Authentic Report
Measurement Database
Verify report
Software
Attestor
Typically trusted hardware components, e.g., TPM
Minimal hardware trust anchors for embedded systems (e.g., SMART [El Defrawy et al., NDSS’12])
Is the prover in trustworthy state?
Verifier (trusted)

## Slide 3: Assumptions & Limitations of Current Attestation Schemes
Static, i.e., ensures the integrity of binaries but not of their execution
  Room for runtime attacks
Software-only attacks

## Slide 4: Runtime Attacks
A
B
D
C
E
F
X
E
A
B
D
C
F
A
B
D
C
E
F
Data Execution Prevention
(DEP)
Control Flow Integrity (CFI),
Code Randomization
Code Injection
Code Reuse
Data Only
isAdmin=0
isAdmin=1
Notes: Hard to solve

## Slide 5: One step further .. Control-flow Attestation

## Slide 6: Related Work: Control-Flow Attestation (C-FLAT) [Davi et al., CCS 2016]
Online: Runtime Validation
P1
P2
LP1
Measurement Database
Offline: Control-Flow Graph (CFG) Analysis & Path Measurement
P*x
P*2
Processor
Secure World
Normal
World
instrumented branches
(Execute
App A)
(Measure &
Attest)
Challenge
Instrumented App A
Attest then Execute
Trusted component
Notes: In order to mitigate non-control-data attacks, runtime control-flow attestation has been proposed by Davi et al. in CCS 2016.

## Slide 7: Limitations of C-FLAT
Intensive code instrumentation required
Attestation overhead increases linearly with the number of control-flow events: huge overhead for some code samples
Overhead due to:
  Trampolines (instrumented branches)
  Context switching between normal and secure worlds
  Hash calculations
Hardware asistance?
Notes: The scheme proposed is software-based and requires that the code is heavily instrumented by trampolines at every branch instruction to capture the branches. This increases code size and contributes to the attestation overhead. The attestation overhead increases linearly with the number of controlflow events which means it can be huge for some code samples.
Besides trampolines, the overhead is due to the context switching between normal and secure worlds of the TEE since the measurement has to be performed i a trusted environment and due to the cntext switching for the hash computations themselves.
These limitations make it very challenging to deploy C-FLAT in real-world constrained scenarios. And the question now is can we do better?

## Slide 8: Related Work: HW-based Control-Flow Attestation (LO-FAT) [Dessouky et al., DAC 2017]
Offline: Control-Flow Graph (CFG) Analysis & Path Measurement
Online: Runtime Validation
HW Engine
Hash
Controller
P1
P2
LP1
Measurement Database
Processor
P*x
P*2
Control - Flow Attestation
App A
Attest then Execute
Trusted component
Challenge

## Slide 9: What about physical attacks?

## Slide 10: More Realistic Adversary: TOCTOU Attack
Challenge
Authentic Report
Attestation scheme
Processor
Malicious
controller
App A
Malicious App
Execute
Attest
Attest then Execute
Trusted component
Untrusted component
Notes: Malicious

## Slide 11: ATRIUM: Big Picture
Offline: Control-Flow Graph (CFG) Analysis & Path Measurement
Online: Runtime Validation
HW Engine
Hash
Controller
Challenge
P1
P2
LP1
Measurement Database
Processor
P*x
P*2
Runtime Attestation
Trusted component
Untrusted component
App A
Attest and Execute

## Slide 12: ATRIUM: Our Contributions
Memory bank attacks on current attestation schemes for embedded devices
Detect memory bank attacks & software runtime attacks
Prevent software attacks on the attestation process itself
No software instrumentation required
Proof-of-concept implementation and evaluation targeting RISC-V core
A hardware-based scheme for runtime attestation

## Slide 13: Adversary Model & Assumptions
An attacker, has physical access to the prover
  Can manipulate off-chip memroy contents
An attacker can perform software attacks including runtime attacks
  No prevention mechanisms are assumed, i.e. no DEP or CFI.

## Slide 14: Example: Offline Phase
Control-Flow Graph (CFG) Analysis & Path Measurement
N1
N2
N3
N5
N7
N4
N6
Segment 1 | Segment 2 | Segment 3
Nn represents the address of the block and instructions of that block
H1= H(N1||N3||N7||N4)
H2= H(N1||N2)
H3 = H(N5||N6)
H4 = H(N4)

## Slide 15: Example: Online Phase
N1
Nn represents the address of the block and instructions of that block
Hash
Instruction
filter
Hash memory
H1
N2
N1
N2
N3
N5
N7
N4
N6
ARTRIUM HW- Components
Of-the-shelf
Components
Challenge: How to handle loops efficiently?

## Slide 16
N6
Hash lookup
...
H3
.....
.....
Branch (source, target)
Hash
Instruction
filter
Loop detection
Hash memory
N5
loop_id
H3
Address(H3), increment counter
Nn represents the address of the block and instructions of that block
N1
N2
N3
N5
N7
N4
N6
ARTRIUM HW- Components
Of-the-shelf
Components
Example: Online Phase
Challenge: How to detect loops at runtime?
  Without code instrumentation
  No instruction set extension

## Slide 17: ATRIUM: Detailed Architecture
Hash
PC,
executed instruction
Hash memory
hash
Hash lookup
Loop encoder
Processor Pipeline
Instruction buffer
hash
increment hash counter
loop_ID, F_ID, executed instruction
branch (SRC, TGT), executed instruction
loop_ID,
F_ID
Hash controller
loop_status, loop_ID
instruction
P (inb,inm)
H0ǁ... ǁHn
Legend
ARTRIUM HW- Components
Of-the-shelf
Components
Instruction filter

## Slide 18: Detecting Loops
44c: sw a5,-24(s0)
45c: j 47c <fun1+0x40>
460: lw a5,-40(s0)
464: addi a5,a5,1
474: addi a5,a5,1
480: li a5,9 #9
484: ble a4,a5,460 <fun1+0x24>
488: lw a5,-20(s0)
assembly
backward non-linking branch: loop entry detected!
We develop a heuristic in which every non-linking branch to a backward memory address is interpreted as loop entry
Suitable for RISC architectures
Notes: ATRIuM uses a simple heuristic
to differentiate between backward branches that constitute loops,
and branches for subroutine calls where the call target resides earlier
in memory. Since subroutine calls use instructions that update the
link-register, we consider the target of each non-linking backwards
branch as a loop entry node.
We base our heuristic on
our observations of the RISC-V compiler assembly and the calling convention described in the instruction manual: any subroutine call
with multiple call sites must be linking and updates the link-register.
Subroutines with a single call site are still compiled as a linking
branch or are optimized by traditional inlining using the RISC-V
compiler.

## Slide 19: ATRIUM: Detailed Architecture
PC,
executed instruction
Hash memory
hash
Hash lookup
Loop encoder
Processor Pipeline
Instruction buffer
hash
increment hash counter
loop_ID, F_ID, executed instruction
branch (SRC, TGT), executed instruction
loop_ID,
F_ID
Hash controller
loop_status, loop_ID
instruction
P (inb,inm)
H0ǁ... ǁHn
Legend
ARTRIUM HW- Components
Of-the-shelf
Components
Instruction filter
Hash

## Slide 20: Hash function: Blake2
Blake2
1024-bit block
88-bit Hash
Input: multi-block messages
  Each block holds up to 32 words (addresses or instructions)
Output: configurable
  set output length to 88 bits (reasonable security guarantees & area overhead)
Throughput: 24 cycles to process one block
  Stalls are due to successive messages with less than 24 words
Notes: Takes as input multi-block messages and produces one hash value
Each message block is 1024-bit
  Each block can hold up to 32 words (addresses or instructions)
The output of the hash is configurable
  We set the output length to 88 bits (reasonable security guarantees & area overhead)
Throughput: 24 cycles to process one block
  Stalls due to successive messages with less than 24 words

## Slide 21: Implementation
Proof-of-concept RTL implementation of ATRIUM interfacing with Pulpino1: first open-source RISC-V2 SoC
No ISA extensions or binary instrumentation required  portable and legacy software compliant
1 http://www.pulp-platform.org/
2 https://riscv.org/

## Slide 22: Evaluation
Cycle-accurate Modelsim simulation of the RTL while executing benchmarks on Pulpino core
Guaranteed fine-grained control-flow recording
Maximum operating clock frequency on par with Pulpino (70 MHz)
Resources Utilization: (depends on configuration)
  Area: 15% registers (15K) and 20% LUTs (10K) on Virtex-7 XC7Z020
  Memory: 1 Block RAM (BRAMs)
Notes: Cycle-accurate Modelsim simulation of the RTL while executing code segments on Pulpino
  synthetic code segments
  code segments from real-world application: Syringe Pump (source: https://hackaday.io/project/1838-open-syringe-pump
No overhead on executing software while not compromising security guarantees
  processor does not stall due to LO-FAT operation
  LO-FAT guaranteed not to drop control-flow events  complete control-flow recording
  iterations of each unique loop path executed reported
  indirect branch targets reported
    Large due to sparse loop path-indexed memories that ensure constant-time single-cycle access
    Optimized implementation in progress using CAMs consumes significantly less memory!

## Slide 23: Performance Overhead of selected Benchmarks
Chart: Percentage of additional cycles
| Dhrystone | mt-matmul | rsort | spvm | towers
Benchmarks | 0.0197 | 0.1223 | 0.2269 | 0.0606 | 0.017

## Slide 24: Conclusion and Future Work
Typical attestation schemes are vulnerable to physical TOCTOU attacks as well as software runtime attacks
We proposed ATRIUM to detect such attacks with reasonable overhead
Investigate the applicability of ATRIUM to network of autonomous devices

## Slide 25: Thanks for your Attention 